## Slide 1: NeXOS development and end-to-end integration of compact, low-power, multifunctional ocean sensors
Eric Delory, Dr.-Ing.
Oceanic Platform of the Canary Islands (PLOCAN) PLOCAN Observatory NeXOS Project coordinator eric.delory@plocan.eu

## Slide 2: NeXOS
Ocean of Tomorrow Project
Project number : 614102 (FP7-OCEAN-2013.2)
Starting date : 1st of October 2013 (48 months)
21 partners from 6 European countries
Coordinator : Eric Delory (PLOCAN, Spain)

## Slide 3: NeXOS innovations
Transversal:
Smart sensor interface
Antifouling (optics)
End-to end Interoperability via OGC standards
Application-specific:
Multifunctional optics
Preprocessed passive acoustics
Ecosystem sensors for EAF (fisheries)

## Slide 4: NeXOS Objectives
  Lower capital and operating expenses for sensor systems and in-situ ocean observations
  Multifunctional sensor packages for multiple cost-effective platforms
  Standard web interfaces (Sensor Web)
  Extend the deployment duration of sensors

## Slide 5: Sensors, Platforms and Oceanscape

## Slide 6: NeXOS & MSFD GES

## Slide 7
Sensor Technology |  |  | Sensor type | 
Optical |  |  | O1 Matrix-fluorescence | 
 |  |  | O2 Hyperspectral | 
 |  |  | O3 Carbon | 
Passive Acoustics |  |  | A1 Preprocessed | 
 |  |  | A2 Real-time | 
RECOPESCA/EAF |  |  | EAF/ Chlorophyll | 
 |  |  | EAF/Oxygen | 
Cross-cutting Technologies |  |  |  | 
Smart Sensor Interface – OGC PUCK + SWE |  |  | Bio-fouling prevention | 
Target Platforms |  |  |  | 
Gliders | Drifters/profilers | Cable Observatories |  | Ferries
Trawlers | Nets & Lines | Other leisure |  | Stand alone

## Slide 8: From basic principles to operational systems
Technology Readiness Levels

## Slide 9
Research to Prove Feasibility (TRL 2&3)
System commissioning (TRL 7&8)

## Slide 12: NeXOS O1 – Fluorescence matrix TRL 5 to 7
 | Em |  |  | 
Ex | 460 | 655 | 682 | 850
375 | CDOM | CDOM backgnd | CDOM backgnd | 
470 | scat 460 |  | chl-a | 
625 |  | cyanobac pig. | PC via chl-a | 
850 |  |  |  | Turbidity
 | Em |  |  | 
Ex | 280 | 360 | 450 | 850
254 | PAH(a) | PAH(b) | CDOM(A) | 
280 | scat 280 | PAH(c) | CDOM(B) | 
320 |  |  | CDOM(C) | 
850 |  |  |  | Turbidity
UV-Version:
PAH monitoring CDOM classification
VIS-Version: algae, CDOM, turbidity monitoring

## Slide 13: NeXOS O1 – Fluorescence matrix TRL 5 to 7

## Slide 14
Conductive SnO2 electrode
Copper
Window
NeXOS Biofouling protection by electro-chlorination
TRL 4 to 7
Electrochlorination by SURFACE thin film working electrode on window
Image and information courtesy of Laurent Delauney, IFREMER
Protected
Unprotected

## Slide 15
NeXOS O2 – Hyperspectral Cavity Absorption sensor TRL 4 to 5

## Slide 16: Phytoplankton Identification with NeXOS O2
Currently, reliable identification of at least 7 groups possible (in lab experiments)
  Chlorophytes
  Chrysophytes
  Cryptophytes
  Bluegreen cyanobacteria
  Brown cyanobacteria
  Prochlorococcus
  Browngreen algae (Diatoms, Dinophytes, Haptophytes)
Differences also visible in field data (further validation necessary)
Improvement of the algorithm by inclusion of field spectra in the reference database

## Slide 17: NeXOS O3 – Carbon Sensor System TRL 4 to 7
Spectrophotometric pH detection,
with embedded system
(Raspberry pi 2,linux ARM7 arch.)
8 ADC channels.
Embedded PUCK friendly.
Different Array Setups:
Cbon2-fb pH and pCO2 in the same box aside the ferrybox system on a ship
Cbon2-sv pH and low power NDIR pCO2 in the same surface vessel (sailbuoy)
Cbon3-fb: pH + pCO2 + AT

## Slide 18: Recopesca

## Slide 19: NeXOS new Recopesca sensors TRL 3 to 7 (status: 5)
Oxygen Sensor
Fluorometer Sensor (chl-a)
Sensors to test
CTD (ref)

## Slide 20: NeXOS Acoustic Sensors TRL 2 to 8 (current:6)
NeXOS A1: Compact low-power multifunctional passive acoustics sensor system, enabling on-platform measurement and characterisation of underwater noise for platforms with limited communication.
NeXOS A2: Compact multifunctional sensor system for real-time waveform streaming aimed for platforms with unlimited autonomy and/or communication capability.

## Slide 21: Passive Acoustic Sensors

## Slide 22: NeXOS Acoustic Sensors TRL 2 to 8 (current:6)
Compact, low power <1W in active mode (low power) for autonomous mobile platforms
OGC-PUCK and SWE enabled

## Slide 24: Web of Things OGC SWE and OGC PUCK open standards TRL 4 to 7

## Slide 25: Web of Things Smart Sensor Interface TRL 3 to 8
Smart Sensor Interface and Web Components Hardware and software interface with miniaturized low power modular design
Implementation of OGC PUCK protocol for instrument discovery and identification
Precision Time Protocol (IEEE Std. 1588) for time synchronization
Open Source software development tools
Open Data access based on Sensor Web Enablement framework.
Notes: SPS is sensor planning service; SOS sensor observation service; SAS sensor alert service; Sensor Interface Descriptor (SID) schema that enables the declarative description of sensor interfaces, ... a profile and extension of SensorML. Based on this schema, SID interpreters can be implemented, independently of particular sensor ..

## Slide 26: SM(i)LE

## Slide 31: NeXOS SWE User front end

## Slide 32: NeXOS Test and Demo Scenarios
Scenario 1: Hydrocarbon observations with gliders; detection and quantification of leakage
Scenario 2: Carbon cycle and carbon sequestration monitoring with ferry-boxes including pH, inorganic carbon, carbonate ions, partial pressure CO2.
Scenario 3: Passive acoustic monitoring and characterization of underwater sounds from floats and gliders
Scenario 4: Observations for sustainable fisheries observing ocean variables
Scenario 5 : Detection and characterization of phytoplankton blooms and groups

## Slide 33: Status & Next Steps
  Tests, validation and demonstrations on PLOCAN testbed and observatory, Norwegian Sea, Mediterranean Sea
  Continuum with EMSO (EMSODev), FixO3 (R&D and harmonisation), AtlantOS (WP6)

## Slide 34: PLOCAN Wave glider with OGC-PUCK, SWE Bridge and NeXOS sensors

## Slide 35: Argo float (Provor) with A1, Seaexplorer with A1 and O1 miniflu – OGC SWE & PUCK enabled

## Slide 36: Ferrybox and sailbuoy with pCO2 and pH

## Slide 37
Thank you!
www.nexosproject.eu
eric.delory@plocan.eu
"
Work presented was funded by project NeXOS (Grant Agreement No. 614102)

## Slide 38
Thank you!
www.nexosproject.eu
eric.delory@plocan.eu