## Slide 1
F. Gabriel Acién.
Dpt. Chemical Engineering, University of Almeria, SPAIN
Introduction to microalgae-based biofertilizers produced with circulated nutrients
Notes: Thanks for inviting me to talk about SABANA Project, focused into the sustainable production of end products for agriculture and aquaculture from microalgae

## Slide 2
Biopesticides
Aim
Biopesticides
Biostimulants
Biofertilizers
Notes: Thus, in the presentation we will shortly revise the fundamental of mass transfer, then studying its relevance on the design and operation of two of the main types of photobioreactors, open raceway and tubular photobioreactors.

## Slide 3
Agriculture applications
Agriculture related applications
Plant biostimulants
Definition:
A plant biostimulant is any substance or microorganism applied to plants with the aim to enhance nutrition efficiency, abiotic stress tolerance and/or crop quality traits, regardless of its nutrients content.
Main categories of plant biostimulants:
Humic and fulvic acids
Protein hydrolysates and other N-containing compounds
SEAWEED EXTRACTS and botanicals(=plant extracts)
MICROALGAE incl. CYANOBACTERIA
Chitosan and other biopolymers
Inorganic compounds
Beneficial fungi
Beneficial bacteria
Plant fertilizers
Definition:
A fertilizer is any material of natural or synthetic origin that is applied to soil or to plant tissues to supply plant nutrients. Fertilizers may be distinct from liming materials or other non-nutrient soil amendments. Many sources of fertilizer exist, both natural and industrially produced. For most modern agricultural practices, fertilization focuses on three main macro nutrients: Nitrogen (N), Phosphorus (P), and Potassium (K) with occasional addition of supplements like rock dust for micronutrients. Farmers apply these fertilizers in a variety of ways: through dry or pelletized or liquid application processes, using large agricultural equipment or hand-tool methods.
Notes: Thus, in the presentation we will shortly revise the fundamental of mass transfer, then studying its relevance on the design and operation of two of the main types of photobioreactors, open raceway and tubular photobioreactors.

## Slide 4
Biofertilizers market
Large volumes are required
Low prices are required
Microalgae can be used as biofertilizers in the case of being produced at zero cost during wastewater treatment processes, otherwise it is not cost competitive for this application
7%N
1.5%P
0.5%K
7%N
1.5%P
0.5%K
Agriculture applications
Notes: Thus, in the presentation we will shortly revise the fundamental of mass transfer, then studying its relevance on the design and operation of two of the main types of photobioreactors, open raceway and tubular photobioreactors.

## Slide 5
Biostimulants market
Market of agriculture products is confirmed for biostimulants related products
Microalgae based products are scarce but highly appreciated, major problem being the low amount of biomass available and high cost
Biomass production cost<10 €/kg
Minimum capacity>20 tn/year
Agriculture applications
Notes: Thus, in the presentation we will shortly revise the fundamental of mass transfer, then studying its relevance on the design and operation of two of the main types of photobioreactors, open raceway and tubular photobioreactors.

## Slide 6
Biostimulants
Effects of algal extracts on plants
(Michalak, I., et al. (2017) Molecules 22, 66.)
Major effects:
Improvement of soil
Resistance to stress
Regulation fo growth/fruits
Reduction of requirements
Agriculture applications
Notes: Thus, in the presentation we will shortly revise the fundamental of mass transfer, then studying its relevance on the design and operation of two of the main types of photobioreactors, open raceway and tubular photobioreactors.

## Slide 7
Biostimulants from algae
Agriculture applications
Notes: Thus, in the presentation we will shortly revise the fundamental of mass transfer, then studying its relevance on the design and operation of two of the main types of photobioreactors, open raceway and tubular photobioreactors.

## Slide 8
Biostimulants compounds
Most relevant compounds:
Polysaccharides/carbohydrates
Peptides and amino-acids
Phytohormones (auxin, citokinin, gibberelin)
Amino-acids
Phytohormones
Agriculture applications
Notes: This project is supported by the EU Commission on the Blue growth program, and it is an innovation action coordinated by the University of Almeria in collaboration with industrial partners as Aqualia, Biorizon, GEA Westfalia and Veronessi, in addition to academic partners as university of Milano, Szechenyo university, AlgaTech, KIT and University of Gran Canaria, in addition to CIB.

## Slide 9
Sustainable production
Development of industrial processes
UNIVERSITY OF ALMERIA
R&D FACILITY
PRODUCTION FACILITY
1.000 -5.000 m2 surface
Notes: This project is supported by the EU Commission on the Blue growth program, and it is an innovation action coordinated by the University of Almeria in collaboration with industrial partners as Aqualia, Biorizon, GEA Westfalia and Veronessi, in addition to academic partners as university of Milano, Szechenyo university, AlgaTech, KIT and University of Gran Canaria, in addition to CIB.

## Slide 10
Sustainable production
Wastewater as nutrients source
Effluent | COD/BOD, mg/l | N, mg/l | P, mg/l | Total Suspended Solids, mg/l | Turbidity, NTU
Digestate | 9000/7000 | 8000 | 400 | 10000 | 30000
Manure | 16000/12000 | 9000 | 500 | 3000 | 9000
Agro-industrial (Breweries) | 4000/3800 | 30 | 10 | 1000 | 3000
Centrate | 300/200 | 500 | 12 | 1000 | 3000
Sewage | 700/500 | 65 | 11 | 300 | 900
Microalgae culture medium |  | 50 | 10 | 0 | 0
The composition of sewage and centrate are similar to standard microalgae culture media, but digestate and manure contain too much contaminants
Microalgae can be produced using whatever of these wastewater as only nutrients source, recovering up 90% of nutrients inlet
Notes: This project is supported by the EU Commission on the Blue growth program, and it is an innovation action coordinated by the University of Almeria in collaboration with industrial partners as Aqualia, Biorizon, GEA Westfalia and Veronessi, in addition to academic partners as university of Milano, Szechenyo university, AlgaTech, KIT and University of Gran Canaria, in addition to CIB.

## Slide 11
Sustainable production
Overall capacity is a function of nutrients source
Both biomass production and wastewater treatment capacity is a function of composition of the wastewater, mainly N/P concentrations
Capacity of the process is limited by the performance of photosynthetic reaction
Chart: Nitrogen concentration (mg/L), Biomass production (kg/m3)
| Digestate | Manure | Centrate | Breweries | Sewage
Nitrogen concentration | 8000 | 9000 | 500 | 30 | 65
Biomass production | 56 | 63 | 3.5 | 0.21 | 0.455
Treatment capacity | 5.3571 | 4.7619 | 85.7143 | 1428.5714 | 659.3407
Notes: This project is supported by the EU Commission on the Blue growth program, and it is an innovation action coordinated by the University of Almeria in collaboration with industrial partners as Aqualia, Biorizon, GEA Westfalia and Veronessi, in addition to academic partners as university of Milano, Szechenyo university, AlgaTech, KIT and University of Gran Canaria, in addition to CIB.

## Slide 12
Sustainable production
Industrial demonstrators
Hellín
Almería
Chiclana
Mérida
20,000m2
22,200m2
3,000m2
10,000m2
Notes: This project is supported by the EU Commission on the Blue growth program, and it is an innovation action coordinated by the University of Almeria in collaboration with industrial partners as Aqualia, Biorizon, GEA Westfalia and Veronessi, in addition to academic partners as university of Milano, Szechenyo university, AlgaTech, KIT and University of Gran Canaria, in addition to CIB.

## Slide 13
Sustainable production
Industrial demonstrators
REUSING EFFLUENTS FROM AGRICULTURE TO UNLOCK THE POTENTIAL OF MICROALGAE (GA 101060991)
HORIZON-CL6-2021-CIRCBIO-01-09 — Unlocking the potential of algae for a thriving European blue bioeconomy. Innovation Action . TRL 7
Distributed production of microalgae recovering nutrients from drain water and integrated valorization in foods production systems (agriculture and aquaculture)
Notes: This project is supported by the EU Commission on the Blue growth program, and it is an innovation action coordinated by the University of Almeria in collaboration with industrial partners as Aqualia, Biorizon, GEA Westfalia and Veronessi, in addition to academic partners as university of Milano, Szechenyo university, AlgaTech, KIT and University of Gran Canaria, in addition to CIB.