## Slide 1
SCHeMA: FP7-OCEAN 2013.2-Grant Agreement 614002
SCHeMA integrated in Situ Chemical MApping Probes:
open and modular in situ sensing solution

## Slide 2: Intro
Partners.
Partners organization name
Country
1
Université
de Genève (UNIGE)
Switzerland
2
IDRONAUT
S.r.l
. (IDRO)
Italy
3
Universitaet
Ulm (UULM)
Germany
4
Technische
Universitaet
Graz (TUGRAZ)
Austria
5
Ecole
Polytechni
que
Fédérale
de Lausanne
(EPFL)
Switzerland
6
Nanomateriales
y
Polímeros
S.L.
(
nanoMyP
)
Spain
7
Université
de Bordeaux (UBX1)
France
8
Università
degli
Studi
di
Genova
(
UNIGe
-
IT
)
Italy
9
ETT
S.r.l
(ETT)
Italy
Università
degli
Studi
di Genova
Starting date: 1st October 2013 (48 months)
Total budget: € 6.74 Million
EC contribution: € 5.20 Million
SCHeMA : FP7-OCEAN 2013.2-Grant Agreement 614002

## Slide 3: Objectives
An open and modular sensing solution for in situ high resolution mapping of a range of anthropogenic and natural chemical compounds coupled to master bio-physicochemical parameters
METALS
PESTICIDES
PHARMAS
PATHOGENS
Time
BIO-ACCUMULATION
BIO-AMPLIFICATION
NUTRIENTS
CO2
OIL SPILLS, E-WASTE.....
CLIMATE CHANGE
EUTROPHICATION
PHYCOTOXINS
(HARMFUL) ALGAL BLOOM
O2 DEPLETION
PHYCOTOXINS
Notes: The main objective of the schema project Is to provide an open and modular sensing solution for in situ high resolution mapping of a range of anthropogenic and natural chemical compounds coupled to master bio-physicochemical parameters. The target are chemicals that affects marine ecosystem, living resources and of course human being having interactions.
All of this should be done by implementing new specific sensors, an adaptive probe network, and an ad hoc networking solutions connecting the remote sensors to a land station and a web server for data management and access.

## Slide 4: Objectives
SCHeMA open and modular wireless sensing solution
Plug-and-play adaptive chemical sensor probes
gathering detailed spatial and temporal information (second to hours)
An ad-hoc ICT wireless networking solution
Web-based front-end data information system
System localization, status & (re)configuration
Data transfer & storage
data validation, display, access & download

## Slide 5: Objectives
Development of an array of novel chemical sensors taking advantage of various innovative analytical solutions.
Incorporation of the novel sensors into miniature, rugged, low power consumption, multichannel probes based on Eco-Design-ISO/IEC standards, EnOcean technology as well as energy harvesting devices.
Development of dedicated wired/wireless communication network and web-based front-end system compatible with EU standard requirements (OGC-SWE, SOS, INSPIRE, EMODnet, GEOOS, SEIS).
Evaluation, validation and demonstration of the SCHeMA individual sensing tools and integrated system via short and long-term field applications in Atlantic and Mediterranean coastal areas.
Exploitation & Dissemination

## Slide 6
SCHeMA open and modular sensing solution
(Functionalized) GIME arrays based miniaturized multi-channel voltammetric probe | Bioavailable fraction of: Hg(II), As(III), As(V), Cd(II), Pb(II), Cu(II), Zn(II) | UNIGE, EPFL, Idronaut, nanoMyP
Sensors and probes | Targets | Partners
Solid state ion-selective electrodes based integrated electrochemical probe | CO2, carbonate, alkalinity. Nitrate, nitrite, phosphate. | UNIGE, EPFL , Idronaut
Optochemical mid-infrared sensor probe | VOCs | UULM, nanoMyP
Multi-channel optical sensor probe | 8 algae species producing toxins & Biotoxins (Saxitoxin, Ovatoxin) | TUGRAZ, EPFL , UNIGE

## Slide 7
METALSENSORS
PROBE
Direct simultaneous in situ monitoring of :
Cd(II), Pb(II), Cu(II), Zn(II) – Channel 1
As(III) – Channel 2
Hg(II) – Channel 3
Present at sub-nanomolar concentrations (ng/L level)
Potentiostat & preamplifier
RS484 interfaces & memory board
Wireless module
Pressure & Temperature module
3.6V power supply
On-chip antifouling Gel Integrated MicroElectrode arrays (GIME)

## Slide 8: Objectives
ALGA BLOOM - EUTROPHICATION
PHYCOTOXINS - O2 DEPLETION
ELECTROCHEMICAL
PROBE
All-solid-state ISEs
On-line acidification
module
Flow-through cells
Fluidic system components
Desalinator
FLOW CELL 1
LOD: µM to sub-µM
FLOW CELL 2
Notes: All solid state ISEs: CG electrode –
functionalized carbon nanotube ion-to-electron transducing layers
ISM - polymeric membrane incorporated selective ionophores
Flow-through cells incorporating three ISE and one mini-ref. electrode
Desalinator: desalination based on an electrochemical process
Acidification module: based on the flow of proton through a cation exchanger membrane from an acidic solution reservoir to the sample

## Slide 9: Objectives
TOXIC ALGAE
OPTICAL SENSORS
PROBE
8-channel sensing module based on low-cost:
- LEDs
- optical fibers
- photodiodes
- multi-wavelength fluorescence unit
Detection of single cell events
- quantification of average cell density
Using Multivariate Data Analysis (Linear Discriminant An)
- identification/classification of 8 algae classes
- separation of common toxin producing cyanobacteria

## Slide 10: Objectives
VOCs
OPTOCHEMICAL MID- INFRARED SENSORS PROBE
Sensing module
- Flow-through cell
- Planar silver halide (AgX) coated with a
micro-thin enrichment polymer membrane
Detection module
- FT-IR spectrometer
- Stirling-cooled MCT-detector
Lab optimization for detection of:
PAHs
benzene, xylene, and toluene
Notes: Prototype based on:
- FT-IR spectrometer
- Stirling-cooled MCT-detector (MCT: Mercury-cadmium- telluride)
- planar silver halide (AgX) sensing element
coated with a micro-thin hydrophobic enrichment
polymer membrane

## Slide 11: ICT Solution
Communication protocols for
Information about the probes
Data acquired (temperature, salinity, etc…)
Errors or warnings
Configurations
Since there are:
Different probe/sensor type
Different data acquired
Different error type that should be monitored
Different configuration mechanism
COMMON
COMMUNICATION
STANDARD
Data download
Easy access
Probes and Observation Metadata
Different data Format (xml, csv, json, etc..)
Since there are:
Different client needs
Different type of probes and data
COMMON
INTERROGATION
STANDARD
Notes: The first step we had to face was to define the communication protocols for data exchange between the network controller and the land station. The information that should be exchanged are: information about the probes, the data acquired by the sensors, error or warning e and configuration changes that should occur during the sperimentation. All of these are different from one sensor to another both in form, time resolution and so on so it is important to use a common communication standard that can take into account every single aspect.
Since one of the main goal of the ocean of tomorrow project is to promote interoperability at every level we don’t create a custrom standard for communication but used an existing and emerging standard:
The OGC-SWE enables the discovery, exchange, and processing of sensor observations and tasking of sensor systems by means of 3 standards XML encodings (SensorML, O&M, TML) and 4 standards web service interfaces (SOS, SAS, SPS, WNS)

## Slide 12: Sensor Web Enablement
The OGC Sensor Web Enablement (OGC-SWE) enables the discovery, exchange, and processing of sensor observations and tasking of sensor systems by means of 3 standards XML encodings (SensorML, O&M, TML) and 4 standards web service interfaces (SOS, SAS, SPS, WNS)
Sensor Observation Service (SOS): data and metadata on sensors and observations
Sensor Planning Service (SPS): data and metadata on sensor configuration
Sensors Alert Service (SAS): data and metadata on alerts and errors from the sensors and probes
Notes: This is a simple schema that illustrates the communication between the sensors and the SOS interface. We have 4 different modules (ctd, trace metal, nutrients and carbonate, vocs) that communicate with the probe network controller who is in charge of managing the «intelligence» of the probe. It gets the data from the module and then it is in charge of establishing the communication with the SOS interface of the schema web server.

## Slide 13: SCHeMA SOS
SOS 1.0 (stable version in 2014, lots of example – ISTSOS, IOOS, etc..)
  Core profile (GetCapabilities, DescribeSensor, GetObservation)
  Transactional profile (RegisterSensor, InsertObservation)
Custom methods for registering error and changing sensor configuration
  RequestSP
  InsertError
Easier and faster to implement in the framework of the project instead of using full SAS (Sensor Alert Service) and SPS (Sensor Planning Service)
Development of a light SOS interface fully integrated with ETT observing system (used also for EMODnet Physics), easier to mantain, manage and deployed.

## Slide 14: SOS - transactional
RegisterSensor
InsertObservation

## Slide 15: SAS - SPS
InsertError
RequestSP
RegisterSensor response
InsertObservation response
InsertError response
RequestSP response

## Slide 16: Web Interface
http://dataportal.schema-ocean.eu
The SCHeMA Web Front-end allows the user to:
manage probes and experiments
handle alarms and sensor configurations
view and retrieve stored observations and metadata

## Slide 17: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download

## Slide 18: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download

## Slide 19: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download
Alarm list with different colors showing different severity and action performed by the system (high: SMS to the probe owner; medium: email to the probe owner; low)

## Slide 20: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download

## Slide 21: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download

## Slide 22: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download
It is possible to upload a csv file (the template is available for download in the same page) with metadata and data and make it available to the SCHeMA system (only for registered users)

## Slide 23: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download
The QC Editor allows to manually edit the QC flag of each observation according to the SeaDataNet Quality Flag Scale

## Slide 24: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download
http://151.1.25.219:8181/geoserver/emodnet/wms?service=WMS&version=1.1.0&request=GetMap&layers=emodnet:SCHEMA_Platforms&styles=&bbox=-180.0,-90.0,180.0,90.0&width=660&height=330&srs=EPSG:4326&format=image/png

## Slide 25: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download

## Slide 26: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download
Client
Land Stat
Response: service metadata (Capabilities)
GetCapabilities: What service do you provide?
DescribeSensor: what are the characteristics of sensor YYZ?
Response: sensor metadata (SensorML)
GetObservation: give me data recorded by sensor YYZ
Response: observed data (O&M)
http://dataportal.schema-ocean.eu/service/wssos.asmx/SOS?service=SOS&request=GetCapabilities&version=1.0.0
http://dataportal.schema-ocean.eu/service/wssos.asmx/SOS?service=SOS&request=DescribeSensor&version=1.0.0&outputFormat=text/xml&procedure=urn:ogc:def:procedure:schema::S1_TMSM-2
http://dataportal.schema-ocean.eu/service/wssos.asmx/SOS?service=SOS&request=GetObservation&version=1.0.0&observedProperty=sea_water_temperature&offering=exp-14&responseFormat=text/xml&procedure=urn:ogc:def:procedure:schema::S1_TMSM-2

## Slide 27: Web Interface
Data Visualization
Sensor Management
Alarm Management
User Management
Dashboard
Data Submission
QC Editor
Data Access – WMS
Data Access – SOS
Data Access - Download

## Slide 28: Field tests
Arcachon bay monitoring and demonstration
- R/V Planula IV
The Gironde Estuary and
coastal area
and the R/V Thalia
Genoa harbor long-term
field evaluation - CNR-platform
coastal monitoring and
demonstration - R /V MASO
SCHeMA summer school and
and demonstration in mesocosm

## Slide 29: Field tests
SALINITY 37.93; DEPTH 4.2 m
Species relevant to Carbon cycle and Nutrient Sensing Module – CNSM
Genoa CNR platform, Italy, February 2017
Detection level: mM, i.e. concentrations at level of milligram per liter (ppm)
Notes: CNSM: mM means millimolar corresponding to concentrations at level of milligram per liter (ppm)

## Slide 30: Field tests
Three channel bioavailable Trace Metal Sensing Module - TMSM : Arcachon bay, France, May 2017.
DEPTH: 3 m
in situ simultaneous monitoring of the bioavailable fraction of As(III), Cd(II), Pb(II), Zn(II), Cu(II) at various stations (1 hour interval during a 25 hour) - cycle at the station identified by the red star
Results suggest that the main carrier of As(III) in the Arcachon bay is seawater, while Cd(II) and Pb(II) are carried by freshwaters.
Detection level: nM (nanomolar) - As(III) and pM (picomolar) - Pb and Cd,
TMSM can detect trace metals concentration and monitor variation of concentrations at very low level
Notes: TMSM was applied to in situ simultaneous monitoring of the bioavailable fraction of As(III), Cd(II), Pb(II), Zn(II), Cu(II) – copper - at various stations.
Examples of As(III), Cd(II) and Pb(II) concentrations monitored at 1 hour interval during a 25 hour cycle at the station identified by the red star.
These results suggest that the main carrier of As(III) in the Arcachon bay is seawater, while Cd(II) and Pb(II) are carried by freshwaters.
TMSM: nM = nanomolar (As(III) and pM (Pb – lead, and Cd - cadmium) = picomolar corresponding to concentrations at level of nanogram per liter (ppt), i.e. the TMSM has the capability to detect trace metals concentration and monitor variation of concentrations at very low level.

## Slide 31: Field tests
Multichannel Algae Sensing Module – MASM,
Arcachon bay, France, May 2017.
Histogram with relative fluorescence intensity at different excitation wavelengths and final decision based on selection if mainly algae or cyanobacteria a present in the sample
Score plot of the multivariate data analysis (Linear Discriminant Analysis - LDA). The LDA mainly finds algae and dinoflagellates respectively.
The superordinate results at phylum level are the following:
==== =================== =================
.. Identified phylum probability [%]
==== =================== =================
0.00 Miozoa / Dinoflagellate 27.01 (8.46)
1.00 Bacillariophyta 18.71 (5.86)
2.00 Haptophyta 16.70 (5.23)
3.00 Cryptophyta 13.25 (4.15)
4.00 Ochrophyta 12.96 (4.06)
5.00 Chlorophyta 6.32 (1.98)
6.00 Euglenophyta 5.04 (1.58)
7.00 Cyanobacteria 0.00 (0.00)
==== =================== =================
The confidence interval of this analysis is 93.5% and the separation efficiency 96.0% respectively.

## Slide 32
Find more on:
www.SCHEMA-OCEAN.eu
Coordinator:
Marie-Louise Tercier-Waeber
Marie-Louise.Tercier@unige.ch