## Slide 1
Coastal Mapping
WP2 – Share experiences, standards and best practices
ISPRA
carlo.innocenti@isprambiente.it

## Slide 2: WP2: Share Experience, Standards and Best Practices

## Slide 3
Assess consistency of existing vertical datums
Recommend a standard datum for coastal mapping
WP2.1: Vertical datum issues

## Slide 4: Consistency of vertical datum
Questionnaire on VD:
  Height systems on land
  Tidal datums
  Definition of Chart Datum
  Relation of VD to ETRS89
  Developments
Chart Datum (reference level for nautical charts):
LAT (approx)
MSL
Low water

## Slide 5: Towards a standardized datum
ETRS89-GRS80 ellipsoid
  Ellipsoidal referenced surveying
  Data combination on land and sea
  Requires separation models
European Vertical Reference System
  Only available on land
  Based on traditional leveling
  For marine applications realization should include a geoid
Harmonized datum on the maritime basin level
  Requires involvement and commitment of stakeholders
  Baltic Sea Chart Datum 2000 (implemented 2020)
  North Sea and Atlantic: LAT
  Baltic Sea and Mediterranean: MSL

## Slide 6
Analyze different experiences of coastal data acquisitions gathering information about:
Survey site information
Scope of the survey
Type of instruments
Products obtained
Estimation of the costs
WP2.2: Summarize past experience

## Slide 7: The on-line questionnaire
The questionnaire has been developed using LimeSurvey (freeware software) and hosted on ISPRA server from 22/12/2015.

## Slide 8: Structure of the questionnaire
The questionnaire is divided in 3 main pages:
  Study site information
    extension – elevation – morphological characteristics – tidal range – turbidity – Secchi disk
  Survey information
    scope of acquisition – instrument/sensor - platform
  Other information
    product obtained – reference system – IHO standard – survey cost – data availability

## Slide 9: Information gathered
Feedback from 15 partners
645 response to the past experience questionnaire
  487 by excel table
  158 by the on-line form

## Slide 10: Analysis of the distribution of the answers
Where data were collected
With which instrument
For which purpose
At which cost

## Slide 11: Where data were collected

## Slide 12: Instrument : MBES - SBES

## Slide 13: Instrument : LiDAR

## Slide 14: Instrument : Multispectral

## Slide 15: Purpose : Nautical Charting

## Slide 16: Purpose : Spatial Planning

## Slide 17: Purpose : Environmental monitoring

## Slide 18: Purpose : Fishing Commercial

## Slide 19: Purpose : Coastal Management

## Slide 20: COST

## Slide 21: Critical elements emerged
some areas have not been investigated due to the lack of some European member in the partnership
the partners involved are mainly Hydrographic Offices, and their past experiences are focused on nautical charting which creates a bias in the database of the past experience
The “cost” informations were few and dishomogeneous
 | Survey | N° Cost Provided | Cost Max (€/km2) | Cost Min (€/km2) | Cost Mean (€/km2) | Standard deviation
LIDAR | 85 | 25 | 4022 | 352 | 1961 | 1267.1

## Slide 22
The CMP (Coastal Mapping Planner) is designed to help the coastal mapping planning at regional and transnational scale
It will help the EU planners giving indication about optimal survey techniques for different mapping scenarios
WP2.3: Develop and test an algorithm for choosing most appropriate surveying method

## Slide 23
Different detection technologies can be compared in relation to their ability to obtain the desired products, currently :
  3 technologies (MBES, LIDAR & HYPERSPECTRAL)
  9 selectable products
It has a scalable structure that easily permits to add instruments and products
It takes into account the environmental characteristics of the survey area:
  Elevation
  Secchi disk depth
CMP characteristics

## Slide 24
Basic concepts
The CMP uses the fuzzy logic that permits:
a more natural definition of the environmental variables;
to translate more naturally the knowledge of the expert.
Shallow
Shallow

## Slide 25
MBES rules
If water is deep then MBES is suitable
If on land then MBES is not suitable
If water is shallow then MBES is marginal
If water is very shallow then MBES is not suitable

## Slide 26
LiDAR and Airborne Hyperspectral rules
If depth/secchi disk ratio is bad AND not on land then Lidar (or Air. Hyp.) is not suitable
If depth/secchi disk ratio is poor AND not on land then Lidar (or Air. Hyp.) is marginal
If on land then Lidar (or Air. Hyp.) is suitable
If depth/secchi disk ratio is good then Lidar (or Air. Hyp.) is suitable

## Slide 27
 | LiDAR | MBES | Air.Hyp.
Low resolution DSM | Suitable | Suitable | Not Suitable
High resolution DSM | Suitable | Suitable | Not Suitable
High resolution DSM for navigational purposes (Special order/Order 1a) | Not Suitable | Suitable | Not Suitable
High resolution DSM for navigational purposes (Order 1b) | Suitable | Suitable | Not Suitable
Shore line | Marginal | Not Suitable | Suitable
Vegetation presence map | Marginal | Marginal | Suitable
Vegetation cover type map | Not Suitable | Not Suitable | Suitable
Floor Cover Type map | Marginal | Suitable | Suitable
Properties of the Emerged Sediment | Not Suitable | Not Suitable | Suitable

## Slide 33
Define the functions that permit to estimate the cost of a survey for different acquisition technologies and different environmental characteristics
  Analyze the past experiences data
  Discuss the partner knowledge in a working group
WP2.4: Build a technical & economical strategy

## Slide 34
Cost Function: Results
Chart: Survey effort as a function of depth. Lidar and MBES compared (Norwegian Mapping Authority)
| 1 | 2 | 3 | 5 | 7 | 10 | 20 | 30 | 100 | 150 | 200
MBES | 41.5888 | 24.3279 | 15.3248 | 10.0942 | 7.1335 | 4.1589 | 2.4328 | 1.032 | 0.48656 | 0.34522
High Res Lidar | 0.35 | 0.7 | 1.05 | 1.75 | 2.45

## Slide 35
Cost Function: Results
Chart: Cost functions comparison
| 1 | 1 | 2 | 3 | 5 | 8 | 13 | 21 | 34 | 55 | 89 | 144 | 82.5
Lidar (SHOM) | 12219.5 | 12219.5 | 13621 | 15022.5 | 17825.5 | 22030 | 29037.5 | 40249.5 | 58469 | 87900.5 | 135551.5 | 212634 | 126441.75
MBES (Past Experiences) | 10031 | 10031 | 14504.1468 | 17995.8655 | 23615.4526 | 30324.1128 | 39261.0666 | 50671.6324 | 65477.3379 | 84570.1656 | 109249.5644 | 141121.465 | 104929.5308
SBES (Past Experiences) | 23118 | 23118 | 27625.8067 | 30659.878 | 34961.1372 | 39449.7619 | 44692.4025 | 50554.593 | 57219.0102 | 64747.5695 | 73272.9187 | 82918.1149 | 71858.6285

## Slide 36
WP2.4 results
Conclusion: the past experiences are not sufficient to build a reliable cost function valid on the whole of Europe
Possible development: other environmental variables, together with surface, should be investigated to model a reliable function to quantify the time cost of the survey

## Slide 37: WP 2.5 – Sharing platforms
Research of the main platform categories in order to evaluate the possible technical synergy effects
Review sharing platforms through cooperation, and combining efforts in order to maximize the survey potential

## Slide 38: Findings (technical)
Survey once, use multiple times and for different purposes
  Requires high resolution mapping
    While keeping induced errors to a minimum
  Necessitates combining different types of sensors
    To maximize the number of data types collected
  Size matters, near shore surveys limits the types of survey platforms which may be used.

## Slide 39: Findings - mutualisation of means
Combining efforts
  Shared planning may result in improved cross border mapping efficiency
  Predictable income situation for vessel owners
  Unresolved national restriction on both survey permissions and data distribution
Combining tenders
  Increased volume results in reduced price
  Avoids overlapping efforts
  Increase focus on data requirements and standards

## Slide 40: Conclusions
Survey platform of choice is a surface vessel
  The surface is the ideal spot for mapping many data types
    keeping induced errors to a minimum
    maintaining high position accuracy
  Current development of USV ‘unmanned surface vessels’ will significantly reduce survey cost while increasing efficiency.
  New submersible survey instruments holds great promises towards our goal of ‘surveying once, and reusing many times.’

## Slide 41: Conclusions cont.
Varying national restrictions does limit shared efforts
  Permissions required to perform near shore surveys
  Limitations on who may have access to data surveyed
  Differing policy's on what data resolution that may be freely distributed
Combined tenders is still desirable
  Increased focus on cross border issues that need to be resolved
  Reduced price for all stakeholders involved

## Slide 42: Issues to be resolved
Definition of requirements and standards for the different data types
National restrictions on data aquisition and management needs to be adressed

## Slide 43: Thank you!