## Slide 1: EMODnet Bathymetry Technical Infrastructure and methodology

## Slide 4: Compilation of Regional DTMs
Based on Globe software from Ifremer
Tasks performed using Globe
  Quality control
  Data modeling (EMODnet Bathymetry data model and structure)
  Meta data link
  Deconfliction
  Void filling
  Anomaly detection and possible repair
  Export to NetCDF

## Slide 5: EMODnet DTM integration (overview)

## Slide 6: World baselayer is latest addition to EMODnet Bathymetry product
Next slides provide overview of integration process

## Slide 7
rDTM as received from regional coordinators

## Slide 8
Low resolution GEBCO 2019 data set to fill the gaps

## Slide 9
High resolution land data

## Slide 10
Land mask based on OSM

## Slide 11
Land with negative mask applied

## Slide 12
Land and EMODnet rDTM combined

## Slide 13
Coastline set to 0 meters and combined with land

## Slide 14
Low resolution GEBCO added and buffered

## Slide 15
Buffer interpolated

## Slide 16: Difference without and with buffering

## Slide 17: In numbers:
GEBCO 2019 global grid
  15 arc second resolution
  2.7 Billion grid cells
EMODnet 2018 release (Europe DTM)
  3.75 arc seconds (1/16 arc minute)
  5.4 Billion grid cells with 10 data bands each
EMODnet World Base Layer release 1 (EBWB1)
  3 arc seconds (with upsampled EMODnet Europe DTM)
  90 Billion grid cells

## Slide 18: Product generation
All processing steps so far are performed on the data itself. At this stage, no other products have been created
Products (created by GGSgc and Deltares) include:
  Source reference polygons
  Depth contours
  3 RGB tile sets in different colour schemes at 0.00069 arc degree (appr 1/24 arc minute) with hillshading
  High resolution data sets (resolution < 1/16 arc minute) including an polygon index map and RGB images at native resolution
  64 data tiles in 8 different formats
  3 sets of coastlines for different tidal levels based on satellite imagery
  World baselayer RGB tiles rendered in 4 map projections at 0.00069 arc degree resolution with hillshading

## Slide 19: Preparation for visualization
32 bit geotiffs
Post-Processing / Tiling data
PostGIS
Indexing data
Processing of depth data
RGBA GeoTiffs
Tileset
Processing and converting affected images
SSD Storage
Generating WMTS pyramid
Processing of image data
Highly optimized schema

## Slide 20: Services and API
PostGIS
rest.emodnet-bathymetry.eu
ows.emodnet-bathymetry.eu
PostGIS
tiles.emodnet-bathymetry.eu
SSD Storage
WMTS
WMS - WFS
WCS
REST – depth info
Pre rendered raster imagerydata
Vector data
SSD Storage
Raster data
Raster data
https://portal.emodnet-bathymetry.eu/services/services.html

## Slide 21: Depth retrieval services
- Single depth attribute (mean)
Multiple depth attributes (mean, avg, min, max)
Links grid cell with source metadata (source references)
WMS GetFeatureInfo
Bathymetry REST API
{
"min": 105,
"max": 105,
"avg": 105,
"elementarySurfaces": 1,
"smoothed": 104.46,
"smoothedOffset": 0.5400000000000063,
"reference": {
"organisation_id": 540,
"identifier": "S201108200-5",
"type": "CDI"
}
}
{
"type": "FeatureCollection",
"features": [
{ "type": "Feature",
"id": "",
"geometry": null,
"properties": {
"GRAY_INDEX": 543.7899780273438
}
} ],
"totalFeatures": "unknown",
"numberReturned": 1,
"timeStamp": "2020-03-19T10:20:36.836Z", "crs": null
}

## Slide 22: Viewing service

## Slide 23: Hosting
Distributed server infrastructure for production environment
  REST service with depths
  OWS service providing WMS/WCS/WFS
    OWS requests requires processing source data
    Bottleneck: CPU and Disk performance
  WMTS tile service providing static WMTS imagery
    Static, pre-rendered image data
    Bottleneck: Disk performance
    Frequently accessed tiles cached in memory
Backup infrastructure (mirror also used for test purposes)
Use of Amazon AWS services when needed
Physically hosted on Amsterdam Internet exchange

## Slide 24: Thanks Questions?